Office of State Procurement

Rm. 201 General Administration Building, P.O. Box 41017 ( Olympia, Washington 98504-1017 ( (360) 902-7400

http://www.ga.wa.gov

Flooring Materials and Services

Technical Specifications

| pART I: service requirements Each line item must be marked either “as specified” or “described fully.” Failure may result in bid being rejected. Every time your business is unable/unwilling to mark the “check is as specified” box the risk that you bid will be rejected increases. | Check if as Specified | Describe Fully if not as Specified |
| --- | --- | --- |
| CONSULTATION The Contractor shall contact Customer within 2 business days of notification for the purposes of consultation and shall provide the following at no additional charge to the Customer: On-site assessments for product selection, project planning and technical assistance. A Project Plan within 10 business days of site visit. The plan shall include drawings indicating material uses, product layout, installation notes, proposed timeline and cost estimate. Contractor shall be responsible for physical measurements and is responsible for the accuracy of the measurements and the fit of the work. |  |  |
| MATERIAL STORAGE Contractor shall store materials off-site until the original scheduled time of installation at no additional cost to the Purchaser. If the Purchaser postpones the original scheduled installation date for more than 60 days, then the Purchaser may be charged a storage fee which shall be negotiated on a case-by-case basis between the Contractor and Purchaser. Storage facility shall be climate-controlled to maintain all manufacturer-specified storage requirements. Materials must be stored per manufacturer recommendations to prevent crushing or damage. |  |  |
| SITE MANAGEMENT Contractor shall: Coordinate with Purchaser and follow safety and security requirements of the Purchaser. Ensure material deliveries and installations are to be made in a professional manner and in accordance with industry standard best practices. Assure products stored on-site are protected from damage. Not unreasonably encumber the premises with equipment, materials and personnel. When Contractor’s access to a work area conflicts with Purchaser’s operations, the Contractor may be required to reschedule the work to minimize the disruption; this may require performing the work at times other than normal duty hours. Keep site free of accumulated waste, spillage or other debris. Require employees and/or subcontractors to display name badges and whenever possible, the company name shall be visible on the outside of their clothing and on vehicle(s). Assume responsibility for making a thorough survey of the delivery route and installation site to assess necessary delivery, accessibility and installation requirements. |  |  |
| SITE SECURITY Personnel may be required to pass a criminal background check before site access is granted. The Purchaser is to coordinate this activity with Contractor and provide the Contractor sufficient advance notification of this requirement. Contractors or subcontractors providing service at a DOC facility may be required to attend a brief "DOC Security Briefing" prior gaining access to a facility for the first time. |  |  |
| FURNITURE MOVING Removal and Return Contractor shall provide furniture removal and return services and may charge an additional fee for this activity. Typical office furniture shall include but not be limited to desks, filing cabinets, tables, bookcases, credenzas and chairs. All equipment and labor are included in the price. Contractor reserves the right to request that Purchaser arrange for professional movers to remove and return non-typical items, or when the project involves extensive furniture moving. Purchaser reserves the right to contract for furniture removal and return service separate from this contract. Purchaser is responsible for moving computers, telephone equipment and electronic equipment. Lift Service Contractor shall offer a furniture lift service and may charge a fee for this service. Lift System equipment allows installation of Modular Tiles without moving, packing, or disconnecting system furniture. Contractor will be responsible for any damage to the system furniture during the lifting process. All equipment and labor are included in the price. |  |  |
| DELIVERY AND HANDLING Contractor shall transport all materials in a manner that prevents damage and distortion. All materials shall have packaging label listing manufacturer’s name, product name, identification number and related information. Delivery shall be made in accordance with instructions on the Purchase/Field Order from each Purchaser. Contractor shall seek clarification from the ordering agency for any delivery instructions. Equipment Contractor shall provide all necessary equipment and personnel for unloading at the Purchaser’s site. To the extent available, Purchaser may provide equipment and personnel to assist the Contractor in this activity, but ultimately the Contractor is responsible for unloading. Contractor shall ascertain the availability of Purchaser’s equipment or personnel at the time of order placement or prior to scheduled pick-up. Notice Contractor shall provide an advance four (4) weeks delivery notice before shipping, and then follow-up with a three (3) working day final delivery notification. Purchaser shall immediately notify the Contractor of any delays in the schedule and coordinate a new mutually agreeable delivery schedule. Additional Costs There shall be no additional costs to the Purchaser for delivery with the exception of extraordinary situations as defined herein. Extraordinary situations shall be defined as situations in which the nature of the service requires the use special equipment, supplies, or subcontractors, (e.g. barges, airlift, cranes, etc.) that are outside typical or normal delivery/installation parameters. In these rare cases, the Contractor shall obtain prior approval from Purchaser for reimbursement and provide verification of costs upon request. Special Road Permits/Fees or bridge restriction may impact delivery charges for a location. Any fees and permit costs necessary for transportation shall be direct pass through with no additional fees or charges to the Purchaser. Restocking Fees Standard Stock Items: Restocking penalty of 15% plus freight applies if new, unused, in original packaging and shipped back within 30 days of receipt by the Customer. Non-Standard or Custom Items: May not be returned to the Contractor. |  |  |
| removal, recycling and disposal services Contractor shall provide services to remove existing flooring and related materials. Contractor shall provide for dust control and property protection during the removal process. Purchaser shall pre-approve Contractor’s dust control and property protection plans. Contaminants from removal activities may be contained by sealing doors and other openings with tape at head, jamb, and sill. Window exhaust systems to establish negative pressure in contaminant-producing work area, ensuring continuous flow of air into work area may be used. Seal exhaust system ductwork that might leak into building or mechanical systems. Room surfaces (walls, ceilings and floors) shall be left free from dust, dirt and old adhesives, and be left in a condition appropriate to accept new materials. Subfloors (Wood or Concrete) shall be free from dust, dirt and old adhesives in a condition appropriate to accept new flooring (in accordance with the floor preparation requirements described herein). Walls shall be left free from dust, dirt and old adhesives and be left in a condition appropriate to accept new wall base (if applicable). Touch up painting shall be the responsibility of the Customer. Contractor shall dispose of all waste in accordance with federal, state and local laws, permits and regulations. All removed materials shall be removed from the site by the Contractor and disposed of properly. Contractor shall employ best efforts to recycle all materials and to minimize landfills and/or incineration disposal of materials. Contractor agrees to keep written records of its material management at its corporate headquarters so that Purchasers may audit those records upon request, to ensure proper handling and disposition. To the extent allowable by rules and laws, Contractor shall take responsibility and title to all waste materials when the material is in the sole possession of the Contractor. Note on Asbestos: Purchaser shall provide testing for asbestos-containing materials if necessary. Any asbestos abatement will be the responsibility of the Purchaser. All carpet removed within the scope of this contract should not contain asbestos. Carpet Contractor shall provide a recycling program for worn/used carpet and installation scraps. All waste carpet material generated within the scope of this Contract regardless of manufacturer, fiber type or construction must be shipped to a material recovery facility for recycling with exceptions for bio-contamination or hazardous waste which requires proper disposal in accordance with EPA guidelines on hazardous waste disposal. For each order in which carpet is removed, the Contractor shall: Remove used carpet and installation scraps and deposit into a container supplied by a licensed transporter of recyclable materials in accordance with the material recovery facility’s requirements to assure that all materials will be recovered. (Adhesives shall be removed in accordance with the recommendations of the Carpet and Rug Institute (CRI). Adhesive removal solvents shall comply with Carpet and Rug Institute CRI Carpet Installation Standard 2009). Provide the Customer with a certification of product recycling identifying the materials removed, quantities (estimated weight) and disposition of recovered materials (recycled, energy recovery, landfill), and may include identifying specific product components such as fiber type and backing materials. The certificate shall be sent to the Purchaser within sixty (60) days from the date of recycling/disposal, but in no case shall this exceed 365 days from the date of removal. Resilient Flooring and Other Materials Contractor shall remove and legally dispose of existing resilient flooring and other materials (wall base). When feasible, Contractor shall provide recycling of these materials to the greatest extent possible. Reporting Requirements The Contractor shall coordinate with OSP to formulate a mutually-acceptable reporting format for the purpose of monitoring Contractor’s waste management program and tracking material status and disposition within 90 days of award. |  |  |
| FLOOR PREPARATION Floors shall be prepared in accordance with the manufacturer requirements for the product(s) to be installed. Sub-floors/underlayment shall be dry, clean, and smooth per manufacturer requirements. They shall be free from paint, varnish, solvents, wax, oil, and other foreign matter. Installation shall not proceed until sub-floor meets all manufacturer requirements. In the absence of manufacturer requirements for floor preparation, use the CRI Carpet Installation Standard. Standard Floor Preparation Contractor shall provide standard floor preparation at no additional charge to the Customer. Standard floor preparation includes the following: Filling of sporadic hairline cracks 1/8” or less. Filling sporadic small chips and depressions of ¼” deep or less than ¾” in diameter. On wood floors, it includes the filling of sporadic nail or screw holes, and sporadic joints in the plywood substrate of 1/8” or less. Broom sweeping of subfloors that are to receive new flooring. Additional Floor Preparation Circumstances such as structural damage and unusual floor problems which require work beyond the scope of floor preparation as described above shall be identified as Additional Floor Preparation on the Customer’s estimate/quote and will be charged on a case-by-case basis. The time component shall be at the rate for General Labor quoted herein. All Additional Floor Preparation must be approved by the Customer before any charges may be assessed. Purchaser reserves the right to contract for Additional Floor Preparation separate from this contract. Additional Floor Preparation includes: Sanding and scraping residue such as drywall mud, paint overspray, old adhesives etc. Filling or floating rain-damaged concrete slabs. Leveling or skim coating floors. Repair to depressed or raised graining on wood surfaces. Cutting and patching voids or bad wood plugs on wood surfaces. Repairing or re-nailing defective underlayment. |  |  |
| MOISTURE TESTING A successful Bond and Moisture Test and/or Calcium Chloride Test for moisture shall be completed prior to starting all flooring installations at no additional charge to the Customer. These tests shall be performed in accordance with the manufacturer’s requirements and/or ASTM E-1907-04 Standard Practices for Determining Moisture-Related Acceptability of Concrete Floors to Receive Moisture-Sensitive Finishes and ASTM F-1869-04 Standard Test Method for Measuring Moisture Vapor Emission Rate of Concrete Subfloor Using Anhydrous Calcium Chloride. Testing shall be completed at no additional charge to the Customer, except if project conditions require more than two site visits or additional testing. In this case, Contractor is to provide Purchaser with an estimate/quote on a case-by-case basis. Installation shall not proceed until sub-floor meets all manufacturer requirements for moisture. |  |  |
| PROJECT ENVIRONMENT The ambient temperature, humidity conditions, and ventilation requirements shall be maintained in accordance with manufacturer requirements before, during and after installation. All flooring materials shall be conditioned to room temperature as required by the manufacturer prior to starting the installation. Purchaser is to provide as necessary access to water connections, electrical power and lighting to ensure service work can be performed in a safe environment. Purchaser shall provide adequate heating and cooling. |  |  |
| INSTALLATION All installation work shall be performed in a professional workmanlike manner. Unless otherwise specified, all flooring materials shall be installed in accordance with the manufacturer’s installation procedures using the manufacturer-required adhesives and techniques where applicable. In the absence of a carpet manufacturer’s installation procedure, follow the Carpet and Rug Institute’s Carpet Installation Standard. Contractor shall: Be responsible for the acts or omissions of all his or her employees and agents, all other persons performing any of the work, and shall not employ any person to perform the work who is not qualified for the task assigned to him or her. Provide all manufacturer approved tools necessary for a complete installation at no additional charge to Purchaser. Provide manufacturer-approved adhesives no additional charge to Purchaser. Protect carpet and flooring materials against damage and soiling from construction operations and placement of equipment and furnishings during the course of installation. This shall include but not be limited to; providing caution tape and barriers to keep normal traffic off of floors during installation until the area is turned over to the occupant. This does not include permanent protection. Coordinate with Purchaser for the closure of installation spaces to traffic, during and after installation as recommended by the manufacturer. Take all steps necessary to prevent damage to walls, doors, and equipment. To this end, the Contractor shall be responsible for damage to walls, doors, equipment resulting from installation. Touch up painting shall be the responsibility of the Purchaser. Install carpet bars or reducer strips for adjoining other dissimilar floors and/or all other materials and accessories required for a complete installation. Receive no additional compensation for lost, broken, and/or abandoned equipment/tools utilized in the progress of the work. Purchaser shall under no circumstances be responsible for the use, maintenance or damage of Contractor’s equipment. Advise Purchaser on proper installation procedures and effect on warranties when a Purchaser chooses to perform their own installation. Meet with Purchaser upon completion to identify any Punch List items. Any Punch List items shall be completed within thirty (30) calendar days after notice to Contractor, unless the Purchaser grants more time. Final payment may be withheld until all punch list items are completed to the satisfaction of the Purchaser. Carpet Install carpet per pattern and color diagrams flat and tight on sub-floor, well fastened at edges, with a uniform appearance. Install with pile inclination in one direction. The manufacturer will mark each module as to pile direction. Cut and fit carpet neatly into or around breaks, recesses, against bases, casings, door jams, permanent cabinets, equipment, etc. The Contractor shall vacuum entire carpet installation as required by the manufacturer. Installation Method: The direct-glue installation method shall be considered standard installation and included in the material price. Pricing for all other installation methods requiring additional costs and materials (i.e. pad) will be considered on a case-by-case basis and must be approved by the Purchaser. Inset & Border Work: Contractor shall provide carpet inset and border work. Pricing for inset and border work shall be determined on a case-by-case basis and the Contractor shall provide Purchaser with an estimate/quote. All inset and border work and costs must be approved by the Purchaser prior to commencing work. Stair Work: Contractor shall provide carpet stair work for standard waterfall and upholstered steps. Pricing for stair work shall be determined on a case-by-case basis and the Contractor shall provide Purchaser with an estimate/quote. All carpet stair work and costs must be approved by the Purchaser prior to commencing work. Waterfall: A standard waterfall step is any stair with walls on both ends of the step and has no open ends. Upholstered: An upholstered step is any stair with either one or both ends of the step open with carpet that wraps around the open end(s). Resilient Flooring All resilient flooring products shall be installed in accordance with the manufacturer’s installation procedure using the manufacturer-required adhesives (includes wall base, transitions and stair materials). Install per pattern and color diagrams. Cut and fit all joints neatly into or around breaks, recesses, against bases, casings, door jambs, permanent cabinets, and equipment. Ensure all joints and fits to casings, cabinets, or equipment and ensure all cuts are tight, clean and neat. Standard Installation Patterns: Contractor shall provide standard installation patterns at no additional charge to the Purchaser. Tile: Purchaser may choose up to two colors per area or room. Sheet: Purchaser may choose only one color per area or room. Pattern Work: Contractor shall provide patterned installation work for resilient materials. Pricing for patterned work will be determined on a case-by-case basis and the Contractor shall provide Purchaser with an estimate/quote. All patterned work must be approved by the Purchaser prior to commencing any such work. Tile: More than two colors in one area or room. Sheet: More than one color in one area or room. Heat Seam Welding: Contractor shall provide seam welding using heat welding rod. Heat welding rods must be installed and performed according to manufacturer’s instructions using manufacturer’s coordinating welding rod materials and welding accessories. Unit Pricing: Price to be provided on a per lineal running foot unit cost. Integral Flash Coving: The Contractor shall provide flash coving (integral cove) of sheet flooring, by extending the flooring no more than six (6) inches up the wall to form a wall base. This can be accomplished by one-piece flash coving, border flash coving or two-piece flash coving. All Seams in the flash cove area shall be treated the same as seams throughout the rest of the installation. All integral flash coving must be installed and performed according to manufacturer’s instructions using manufacturer-required tools. The Contractor shall provide all required trims and manufacturer-required adhesives. Unit Pricing: Price to be provided on a per lineal running foot unit cost. Integral Flash Cove Corners: The Contractor shall provide (Flash Cove) inside and outside corners. All integral flash cove corners must be installed and performed according to manufacturer’s instructions using manufacturer-required tools. The Contractor shall provide all required trims and manufacturer-required adhesives. All Seams in the flash cove and flash cove corners shall be treated the same as seams and cove throughout the rest of the installation. Unit Pricing: Price for Flash Cove inside and outside corners to be provided on a per each corner unit cost. |  |  |
| CLEANUP Contractor shall: Remove all rubbish resulting from installation at the end of every day; the premises shall be left in a clean condition. Remove excess adhesive, seam sealer and other surface blemishes from floor, base and wall surfaces using manufacturer’s recommended cleaner without damage. Sweep and vacuum entire floor space after installation as recommended by the manufacturer. Leave the work area in clean, safe and operable condition upon project completion. |  |  |
| MAINTENANCE Upon request, the Contractor shall provide written instructions and/or on-site maintenance training for custodial staff at no additional charge to the Customer. |  |  |
| GENERAL LABOR Contractor shall provide an on-site labor charge for general labor. General labor includes but is not limited to additional floor preparation as described herein, miscellaneous repairs, carpet re-stretch services, etc. |  |  |
| WORK HOURS Installation shall be available during standard work hours (6:00 am to 7:00 p.m., Monday - Friday) (not to exceed an 8 hour work shift) and non-standard working hours (evenings, weekends, or holidays). The state anticipates that a majority (approximately 85%) of installations will occur during Non-Standard Hours. Bidders should submit pricing accordingly to accommodate such time frames. Contractor is to coordinate the appropriate hours for installation. |  |  |
| Installation Warranty The installation warranty shall be for a minimum period of two (2) years from the date of substantial completion and shall cover repair or replacement due to defects in the workmanship and shall include all material and labor, including, but not limited to, delivery, installation, removal, reclamation and other related services for all projects which fall within the scope of this Contract. All materials or equipment provided shall be new, unused, of the latest model or design and of recent manufacture. |  |  |

| pART ii: Material requirements: carpet Each line item must be marked either “as specified” or “described fully.” Failure may result in bid being rejected. Every time your business is unable/unwilling to mark the “check is as specified” box the risk that you bid will be rejected increases. | Check if as Specified | Describe Fully if not as Specified |
| --- | --- | --- |
| OVERALL |  |  |
| Testing: All testing must be performed in a NVLAP accredited laboratory. |  |  |
| Indoor Air Quality: Must meet the Green Label Plus (GLP) requirements of the Carpet and Rug Institute (CRI). GLP number must be provided upon request. |  |  |
| Sustainability: Must have third party certification in accordance with NSF 140-2007e Sustainability Carpet Assessment Standard at a “Gold” level minimum. Certificate number must be provided upon request. |  |  |
| Adhesives and Sealants: Must meet the Green Label Plus (GLP) requirements of the Carpet and Rug Institute (CRI). GLP number must be provided upon request. Must meet VOC content standards per South Coast Air Quality Management District (SCAQMD) Rule #1168. All aerosol adhesives must meet the Green Seal Standard GS-36 requirements in effect on October 19, 2000. |  |  |
| Static Charge: ≤ 3.5 kV; when tested in accordance with AATCC 134. |  |  |
| Flammability: Passes DOC-FF-1-70 Pill Test. |  |  |
| Radiant Panel Test: Meets NFPA Class 1; when tested per ASTM E-648 glue down installation. |  |  |
| Smoke Density: NBS Smoke Chamber NFPA-258 - Less than 450 flaming mode. |  |  |
| Construction: Tufted; 100% Synthetic. |  |  |
| Face Fiber: Nylon type 6 or 6,6. |  |  |
| Surface Texture: Cut, Loop, Cut & Loop. |  |  |
| Dye Method: Solution dyed, Yarn dyed, or a blend thereof. Facility-specific requirements will be considerations in determining the type of dye method. |  |  |
| Dimensional Stability (Modular Tile Only): Tiles shall maintain their shape within two hundredths of one percent (.02) when measured on the AACHEN Test. |  |  |
| CATEGORY A (Broadloom & Modular Tile) |  |  |
| Moisture Barriers Required on all Broadlooms: Moisture Barrier = No penetration following the 10,000 Impact Test; uninstalled. |  |  |
| Appearance Retention: CRI TARR ≥ 3.5 CRI TARR = Carpet and Rug Institute (CRI) Texture Appearance Retention Rating (TARR) classification when tested in accordance with ASTM D-5252 Hexapod Drum Test; TARR classification determined using ASTM D-7330. |  |  |
| Warranty: Minimum 25 year non-prorated against (1) wear, (2) static charge, (3) dimensional stability, (4) edge ravel, (5) delamination, (6) tuft bind, (7) adhesion to subfloor, (8) stain resistance, and (9) colorfastness. |  |  |
| Design/Coloration: Contemporary (present date) multicolor patterns and non patterns to accommodate aesthetic requirements ranging from soil hiding to achieving a distinctive/custom look. Provide submittals to accommodate. |  |  |
| category b (Broadloom & Modular Tile) |  |  |
| Performance backings required on all Broadlooms (No Action Back or Unitary) |  |  |
| Appearance Retention: CRI TARR ≥ 3.0 CRI TARR = Carpet and Rug Institute (CRI) Texture Appearance Retention Rating (TARR) classification when tested in accordance with ASTM D-5252 Hexapod Drum Test; TARR classification determined using ASTM D-7330. |  |  |
| Warranty: Minimum 15 year non-prorated against (1) wear, (2) static charge, (3) dimensional stability, (4) edge ravel, (5) delamination, (6) tuft bind, (7) adhesion to subfloor, (8) stain resistance, and (9) colorfastness. |  |  |
| Design/Coloration: Contemporary (present date) multicolor patterns and non patterns to accommodate aesthetic requirements ranging from soil hiding to achieving a distinctive/custom look. Provide submittals to accommodate. |  |  |
| category c (Broadloom & Modular Tile) |  |  |
| Pricing: Multiple price points; all less than any price point in categories A and B. |  |  |
| Appearance Retention: CRI TARR ≥ 2.5 CRI TARR = Carpet and Rug Institute (CRI) Texture Appearance Retention Rating (TARR) classification when tested in accordance with ASTM D-5252 Hexapod Drum Test; TARR classification determined using ASTM D-7330. |  |  |
| Warranty: Minimum 10 year non-prorated against (1) wear, (2) static charge, (3) dimensional stability, (4) edge ravel, (5) delamination, and (6) tuft bind. |  |  |
| Design/Coloration: Contemporary (present date) multicolor patterns and non patterns to accommodate aesthetic requirements ranging from soil hiding to achieving a distinctive/custom look. Provide submittals to accommodate. |  |  |
| warranty definitions |  |  |
| Warranties shall be non-prorated and cover all related costs of replacement including material, freight and labor where the carpet has been installed and maintained in accordance with manufacturer’s recommended guidelines. (All Categories) |  |  |
| Contractor shall be not responsible for damage resulting from abnormal use; water, storm or flood damage; use of improper cleaning agents; and exposure to substances or contaminants which degrade or destroy the face fiber or color of the carpet. Standard: Clear and not just suspected. Product damage must clearly be from storm/flood, improper cleaning agents, and exposure to substances or contaminants as described above. |  |  |
| Wear: Carpet will lose no more than 10% of the face fiber, by weight, during the warranty period. (All Categories) |  |  |
| Static Charge: Carpet will not generate static build up in excess of 3.5 kV, during the warranty period. (All Categories) |  |  |
| Dimensional Stability: Broadloom - Carpet shall not shrink or stretch during the warranty period. (All Categories) Modular Tile - Carpet shall not shrink, stretch, cup, buckle, bubble, edge curl, dome or dish during the warranty period. (All Categories) |  |  |
| Edge Ravel: Carpet will not unravel along seams during the warranty period. (All Categories) |  |  |
| Delamination: Carpet will not delaminate from the secondary backing during the warranty period. (All Categories) |  |  |
| Tuft Bind: Carpet backing compound will securely encapsulate the tuft base during the warranty period (no zippering during the warranty period). (All Categories) |  |  |
| Adhesion to Subfloor: Carpet will bond to a properly prepared subfloor during the warranty period (Subfloor must meet CRI’s recommended floor preparation protocols). (Cat. A & B) |  |  |
| Stain Resistance: Carpet will resist staining from common acidic spills during the warranty period. Spills must be removable using only water or water and a mild detergent such as a neutral spot remover or mild dish soap or by following CRI-recommended protocols. Excludes exposure to substances or contaminants which degrade or destroy nylon fiber or the dye of the carpet. (Cat. A & B) |  |  |
| Colorfastness: Carpet will not lose color due to (1) ozone fading, (2) light fading, or (3) wet/dry crocking during the warranty period. (Cat. A & B) |  |  |

| pART ii: Material requirements: entry systems Each line item must be marked either “as specified” or “described fully.” Failure may result in bid being rejected. | Check if as Specified | Describe Fully if not as Specified |
| --- | --- | --- |
| WALK OFF MATS |  |  |
| Standard Walk Off Mats: Hercules Nop; Mannington Ruffian; or equal. |  |  |
| Premium Walk Off Mats: Bonar Coral Brush; Mannington Recourse; or equal. |  |  |

| pART ii: Material requirements: resilient materials Each line item must be marked either “as specified” or “described fully.” Failure may result in bid being rejected. | Check if as Specified | Describe Fully if not as Specified |
| --- | --- | --- |
| OVERALL |  |  |
| Indoor Air Quality: Must meet FloorScore certification for VOC Emmissions. |  |  |
| Adhesives: Must meet VOC content limit of South Coast Air Quality Management District (SCAQMD) Rule #1168. |  |  |
| Slip Resistance: Must meet the Americans with Disabilities Act Guidelines for static coefficient of friction as manufactured. |  |  |
| vct |  |  |
| Standard Grade: Armstrong Standard Excelon Imperial Texture (1/8 inch thickness); Mannington Essentials or Designer Essentials (1/8 inch thickness); or equal. |  |  |
| Premium Visual Grade: Armstrong Migrations, Stonetex, or Art Effects (1/8 inch thickness); Mannington Brushworks, Solid Point, or Color Point (1/8 inch thickness); or equal. |  |  |
| SHEET VINYL |  |  |
| Heterogeneous (Base Grade): Armstrong Connection Corlon (0.08 inch thickness); Mannington Magna Multiflec; or equal. |  |  |
| Homogeneous (Standard Grade): Armstrong Medintech (0.08 inch thickness); Mannington Bio-Spec; or equal. |  |  |
| Premium Visual Grade: Armstrong Perspectives or Timberline (0.08 inch thickness); Mannington Realities, or Primus; or equal. |  |  |
| linoleum |  |  |
| Linoleum Tile: Forbo Marmoleum MCT (2.0 mm thickness); or equal (2.0 mm thickness). |  |  |
| Linoleum Sheet: Forbo Real (2.5 mm thickness); Armstrong Marmorette, Colorette, or Grannette (2.5 mm thickness); or equal (2.5 mm thickness). |  |  |
| rubber wall base |  |  |
| 4”: 4” Coved toe profile Johnsonite TP series; Roppe 700 Series; or equal. |  |  |
| 6”: 6” Coved toe profile Johnsonite TP series; Roppe 700 Series; or equal. |  |  |
| stair materials |  |  |
| Standard Rubber Tread: Johnsonite raised square disk pattern (RH–SQ) or raised round disk pattern (RH–RD); Johnsonite hammered pattern profile (HMT); or equal. |  |  |
| Stair Riser: To match body color of stair tread, Johnsonite; or equal. |  |  |
| Stair Stringer: To match body color of stair tread, Johnsonite; or equal. |  |  |
| Integrated Tread/Riser: Johnsonite raised square disk pattern (RH–SQ) or raised round disk pattern (RH–RD); Johnsonite hammered pattern profile (HMT); or equal. |  |  |
| transitions |  |  |
| Standard (i.e. Carpet to: Resilient, Concrete, Carpet) Johnsonite, Roppe; or equal. |  |  |
| Premium (Wider; i.e. Carpet to Ceramic Tile, etc) Johnsonite, Roppe; or equal. |  |  |